## Slide 1: Quantitative Evaluation of LoRa for DoD Applications
MAS CAPSTONE Project
Bryce Rooney
University of California, San Diego (UCSD)
Master’s of Advance Study (MAS) - Wireless Embedded Systems

## Slide 2: Lots of Data, Results, and Interpretation….

## Slide 3: Resiliency, Detectability, and Geolocation of a Waveform
Collaboration with Naval Information Warfare Center, Pacific (NIWC Pac) Division 535
Resiliency – How well does a waveform perform in the presence of noise, interference and/or at range?
Detectability – How easy is the presence of the active waveform to detect?
Geolocation – How precise can a transmitter be located?
Resiliency
Detectability
Geolocation

## Slide 4: Long Range (LoRa) Chirp Spread Spectrum (CSS)
  Proprietary modulation technique
  Commercial Off-The-Shelf (COTS)
  Extremely Low Cost, Size, and Power consumption
  Heltec LoRa V3 dev board (Semtech SX1262)
Notes:   Proprietary modulation technique
  Commercial Off-The-Shelf (COTS)
  Extremely Low Cost, Size, and Power consumption
  Modulation uses “Chirps” – linear sweeps in frequency
  Receiver Sensitivity can be below thermal noise floor – valuable for range and resiliency performance
  Heltec LoRa V3 dev board (Semtech SX1262)

## Slide 5: Test Bed and Equipment
Notes: EW cert
RSSI values in ACK, SNR
Other values

## Slide 6: Test Approach
  Iterative testing against various LoRa Configurations
  Spread Factor (SF) and Bandwidth (BW) variations
  Simulated environment
  Resiliency
    Gaussian Noise
    Scenario Driven via Scripts
  Detection
    Radiometry
    MATLAB
    Gaussian Noise
  Geolocation
    Cross Ambiguity Function (CAF)
    MATLAB
SF | BW (kHz) | Ts (ms) | # Sym | Rx Sensitivity (dBm) | Thermal noise estimate (dBm) | SNRmin (Therm noise) (dB) | Effective bps
7 | 10.4 | 12.29 | 125.25 | -134 | -133.6 | -0.4 | 455
7 | 20 | 6.14 | 125.25 | -131 | -130.7 | -0.3 | 911
7 | 125 | 1.02 | 125.25 | -124 | -122.8 | -1.2 | 5,468
7 | 500 | 0.26 | 125.25 | -117 | -116.8 | -0.2 | 21,875
12 | 125 | 32.77 | 70.25 | -137 | -122.8 | -14.2 | 293
12 | 500 | 8.19 | 70.25 | -129 | -116.8 | -12.2 | 1,171

## Slide 7: Development Efforts
  LoRa development boards (Heltec LoRa V3)
  Visual Studio Code C++
  Platform IO extension
  “Application” traffic exercises waveform signal
    50B payload transmitted ~once per second
    ACK/NACK between the two with output logging
  Single code base for quick uploads between test configs
    SF and BW inputs in header file – adjusts dynamically
    Code base works as ACK device or Tx device with button toggle
https://jgromes.github.io/RadioLib/
https://github.com/Brycycle/WES-CAPSTONE
Notes: Published results to find. Google scholar
Connected papers
This weekend.

## Slide 8: Geolocation Results (CAF)
  Top SF 7
    (Left-right) BW 10.4k, BW 20k, BW 125k, BW 500k
  Bottom SF 12
    (Left-right) BW 125k, BW 500k

## Slide 9: Geolocation Analysis
Bandwidth | Peak Area (square km) | Effective Data Rate (SF 7)
10.4 kHz | ~ 80 | ~ 450 bps
20 kHz | ~ 75 | ~ 910 bps
125 kHz | ~ 5 | ~ 5,400 bps
500 kHz | <1 | ~ 21,000 bps
  Detector Location
  Transmitter location
Notes: 4 recorders, 6 2 point CAF outputs combined
No multipath

## Slide 10: Probability of Detection Results
  Slash Curve (Pd = .85)
  SNR = 0 dB
  SNR = -5 dB
  SNR = -10 dB
  SNR = -15 dB
  Radiometry (energy-based detection)
  Empirical Probability Calculations (MATLAB)
  Receiver Operating Characteristic (ROC)
  Data shown: LoRa SF 7 BW 125kHz
Notes: SF7 125k example

## Slide 11: Detection Analysis
Spread Factor | Bandwidth | SNR for .85/.15 (Pd/Pfa)
7 | 10.4 kHz | -5 dB
7 | 20 kHz | -5 dB
7 | 125 kHz | -7.5 dB
7 | 500 kHz | -10 dB
12 | 125 kHz | -7.5 dB
12 | 500 kHz | -10 dB
  Comparison Waveform
  LoRa SF 7 BW 125kHz
  Comparison Waveform = -25 dB SNR
Notes: Independent of WF operation

## Slide 12: Resiliency Results
  Questionable validity of results
  Recursive improvements to testbed, scripts, and codebase desired.
  Deficiencies/limitations:
    Equipment
    Scripts
    Codebase
    Scenario
  SF 7 BW 500kHz Results
  Scenario Visual (Script generated)
Notes: SF7 500k example
RFN resolution of attenuation steps at 2nm increments
RFN handling jam-1 and SNR seen at 1-2
hardcoded scripts only 60nm movement - too short for LoRa?
emulated jammer negligible, but legal and easily obtained
packet vs ber goodut

## Slide 13: Resiliency Analysis
LoRa Config | Starting Distance (X)
SF 7 BW 10.4 kHz | 400 nm
SF 7 BW 20 kHz | 480 nm
SF 7 BW 125 kHz | 390 nm
SF 7 BW 500 kHz | 160 nm
SF 12 BW 125 kHz | 500 nm
SF 12 BW 500 kHz | 480 nm
  SF 7 BW 125kHz Results – Jam SNR greater?
  SF 7 BW 10kHz Results – significant fluctuation, no falloff?
  SF 7 BW 20kHz Results – hard stop and jamming
Notes: Independent of WF operation

## Slide 14: Thank You
Notes: Independent of WF operation