## Slide 1: Quantitative Evaluation of LoRa for DoD Applications
University of California, San Diego (UCSD)
Master’s of Advance Study (MAS)
Wireless Embedded Systems
Bryce Rooney

## Slide 2: Resiliency, Detectability, and Geolocation of a Waveform
Collaboration with Naval Information Warfare Center, Pacific (NIWC Pac) Division 535
Resiliency – How well does a waveform perform in the presence of noise, interference and/or at range?
Detectability – How easy is the presence of the active waveform to detect?
Geolocation – How precise can a transmitter be located?
Resiliency
Detectability
Geolocation

## Slide 3: Long Range (LoRa) Chirp Spread Spectrum (CSS)
  Proprietary modulation technique
  Commercial Off-The-Shelf (COTS)
  Extremely Low Cost, Size, and Power consumption
  Heltec LoRa V3 dev board (Semtech SX1262)
Notes:   Proprietary modulation technique
  Commercial Off-The-Shelf (COTS)
  Extremely Low Cost, Size, and Power consumption
  Modulation uses “Chirps” – linear sweeps in frequency
  Receiver Sensitivity can be below thermal noise floor – valuable for range and resiliency performance
  Heltec LoRa V3 dev board (Semtech SX1262)

## Slide 4: Test Approach
  Iterative testing against various LoRa Configurations
  Spread Factor (SF) and Bandwidth (BW) variations
  Scenario Defined
  Gaussian Noise
  Radiometry
  Cross Ambiguity Function (CAF)
  Scripts
  Simulated environment
  Limitations
  Heltec/LoRa Code development
  Available hardware
  Scripts
  Scenarios

## Slide 5: Development Efforts
  LoRa development boards (Heltec LoRa V3)
  Visual Studio Code C++
  Platform IO extension
  “Application” traffic exercises waveform signal
  50B payload transmitted ~once per second
  ACK/NACK between the two with output logging
  Single code base for quick uploads between test configs
    SF and BW inputs with dynamic protocol adjustment to minimize iterative testing
    Code base works as ACK device or Tx device with button toggle
Notes: Published results to find. Google scholar
Connected papers
This weekend.

## Slide 6: Test Bed and Equipment
Notes: EW cert
RSSI values in ACK, SNR
Other values

## Slide 7: Geolocation Results (CAF)
  Top SF 7
    (Left-right) BW 10.4k, BW 20k, BW 125k, BW 500k
  Bottom SF 12
    (Left-right) BW 125k, BW 500k

## Slide 8: Geolocation Analysis
Bandwidth | Peak Area (square km) | Effective Data Rate (SF 7)
10.4 kHz | ~ 80 | ~ 450 bps
20 kHz | ~ 75 | ~ 910 bps
125 kHz | ~ 5 | ~ 5,400 bps
500 kHz | <1 | ~ 21,000 bps
  Detector Location
  Transmitter location
Notes: 4 recorders, 6 2 point CAF outputs combined
No multipath

## Slide 9: Probability of Detection Results
  ROC Perfect Classifier
  ROC Near-Randon Classifier
  Slash Curve (Pd = .85)
  SNR = 0 dB
  SNR = -5 dB
  SNR = -10 dB
  SNR = -15 dB
  Radiometry (energy-based detection)
  Empirical Probability Calculations (MATLAB)
  Receiver Operating Characteristic (ROC) Curve
  Slash curve
Notes: SF7 125k example

## Slide 10: Detection Analysis
Spread Factor | Bandwidth | SNR for .85/.15 (Pd/Pfa)
7 | 10.4 kHz | -5 dB
7 | 20 kHz | -5 dB
7 | 125 kHz | -7.5 dB
7 | 500 kHz | -10 dB
12 | 125 kHz | -7.5 dB
12 | 500 kHz | -10 dB
  Comparison Waveform
  LoRa SF 7 BW 125kHz
  Comparison Waveform = -25 dB SNR
Notes: Independent of WF operation

## Slide 11: Resiliency Results
  Radiometry (energy-based detection)
  Empirical Probability Calculations (MATLAB)
  Receiver Operating Characteristic (ROC) Curve
  Slash curve
Notes: SF7 125k example

## Slide 12: Resiliency Analysis
  Comparison Waveform = -25 dB SNR
Notes: Independent of WF operation

## Slide 13: Conclusions
  Comparison Waveform = -25 dB SNR
Notes: Independent of WF operation