## Slide 1: Capstone Mid-Quarter Update
UCSD WES MAS
Bryce Rooney

## Slide 2: Agenda
Project Description and Overview
  Methods of Evaluation
  LoRa Waveform
  Current Schedule and Success
  Future Schedule
Test Approach
Development Efforts
Test Bed and Equipment
Results So Far

## Slide 3: Quantitative Evaluation of LoRa Resiliency, Detectability, and Geolocation
Characterize the performance of the LoRa Radio Frequency (RF) Chirp Spread Spectrum (CSS) modulation with methods used by the Department of Defense (DoD).
  Anti-Jam and Range performance
  Probability of Detection
  Probability of Geolocation
Collaborate with Naval Information Warfare Center, Pacific (NIWC Pac) Division 535 to leverage existing facilities and equipment.
Write a research paper on findings with insight into desired (or not desired) characteristics and how this fits into DoD Advanced Tactical Data Links (ATDL) research and development.

## Slide 4: Methods of Evaluation
  Probability of Detection (LPD)
  Geolocation Avoidance
  Anti-Jam and Range Performance

## Slide 5: Probability of Detection
  Methods and Techniques
    Radiometry (energy-based detection)
    Computational-heavy MATLAB Algorithm
    Compares signal to Gaussian noise
  Quantitative Metrics
    Receiver Operating Characteristic (ROC) Curve
      Probability of true positive detections against false positive detections
    Slash curve
      Depicts the relationship between SNR and integration time for a given probability of true detection

## Slide 6: Geo-location Avoidance
  Methods and Techniques
    Cross Ambiguity Function (CAF) Analysis
    Time Difference of Arrival (TDOA)
    Frequency Difference of Arrival (FDOA)
  Quantitative Metrics
    CAF output
    Peak Magnitude and radius

## Slide 7: Anti-Jam and Range Performance
  Methods and Techniques
    Radio Channel Emulator (RCE)
    Live Scripts for RCE control
    Simulated distances and signal level analysis
    Jamming insertion
  Quantitative Metrics
    Range Ratio – Jamming
      ratio of the distance to a friendly receiver versus the distance to a jamming threat
    Range Ratio – Detection
      ratio of the distance to a friendly receiver versus the distance to a threat detector in an LPD environment
Notes: What noise types.

## Slide 8: Long Range (LoRa) Chirp Spread Spectrum (CSS)
  Proprietary modulation technique
  Commercial Off-The-Shelf (COTS)
  Extremely Low Cost, Size, and Power consumption
  Modulation uses “Chirps” – linear sweeps in frequency
  Receiver Sensitivity can be below thermal noise floor – valuable for range and resiliency performance

## Slide 9: Schedule and Progress (May 8)

## Slide 10: Upcoming Milestones
  Test Execution Dates
    Anti-Jam / Range: 8 May
    Geolocation / CAF: 10 May
  Paper Drafting Full Effort
    15 May
  All Data/Metrics exported from Lab
    May 19
  Paper First Draft
    May 24
  Video Presentation Full effort
    May 29
  Paper and Video Submitted
    June 5

## Slide 11: Test Approach
  At set SF how effective is changing the BW?
  At Set BW, how effective is changing the SF?
  At set effective data rate, compare the performance of small SF and short BW against high SF and long BW. (SF7 @ ~25kHz vs SF12 @ 500kHz)
  Compare Results to other waveforms as possible (scrub proprietary and Controlled Unclassified Information (CUI)
  Iterative testing against various LoRa Configurations
  Spread Factor (SF) and Bandwidth (BW) variations
  Other Interpretation:

## Slide 12: Development Efforts
  LoRa development boards (Heltec LoRa V3)
  Visual Studio Code C++
  Platform IO extension
  “Application” traffic exercises waveform signal
  50B payload transmitted ~once per second
  ACK/NACK between the two with output logging
  Single code base for quick uploads between test configs
    SF and BW inputs with dynamic protocol adjustment to minimize iterative testing
    Code base works as ACK device or Tx device with button toggle
Notes: Published results to find. Google scholar
Connected papers
This weekend.

## Slide 13: Test Bed and Equipment
Notes: EW cert
RSSI values in ACK, SNR
Other values

## Slide 14: Results so Far
  Detectability test cases with all LoRa configs
  Met obstacles in RF recording and MATLAB algorithm parameters
  Confirmed valid output metrics.
  All data being processed
  ROC & Slash Curves with Histograms

## Slide 15: Histograms
  SNR 0 dB
  SNR -5 dB
  SNR -10 dB
  SNR -15 dB
  SNR -20dB

## Slide 16: ROC Curve (0 & -5 dB SNR)

## Slide 17: ROC Curve (-10dB SNR)
Notes: Wiki pedia on ROC
Threshhold details

## Slide 18: ROC Curve (-15dB SNR)

## Slide 19: Slash Curve (Pd = .75, Pfa = .25)

## Slide 20: Slash Curve (Pd = .85, Pfa = .15)

## Slide 21: ROC Curve (-10dB SNR)

## Slide 22: Slash Curve (Pd = .95, Pfa = .05)